## Slide 1: Advanced Data Science Programming
3. Arduino & CircuitPython

## Slide 2: Arduino
Open-source electronics platform consisting of a microcontroller with a number of input and output pins
  Easy to use
  Inexpensive
  Low power consumption
  Straightforward programming using C/C++
    Many available libraries, similar to Python
  Hundreds of different boards available from many suppliers

## Slide 3: Arduino Program
Written in C or C++
Two functions:
  setup() – Runs once during board startup
    Used to specify inputs/output modes, initialize devices and variables
  loop() - Runs repeatedly starting when setup() finishes
    Used for the operational code
    When control reaches the end, starts back up at the beginning
      Important to let it reach the end since some boards do timing/cleanup/other management tasks between loops

## Slide 4: Input/Output
Input/Output uses electrical connection points – pins
  Must select:
    Digital or Analog
    Input or Output
Each board runs at a specific voltage - Vcc
  3.3v
  5v
  12v (very rare)
Higher voltage can damage the board
Lower voltage typically won’t cause damage, but also won’t operate correctly

## Slide 5: Input/Output Types
Analog – state is any point along a scale
Digital – state is either on or off
Input – detects if voltage is above/below threshold
  Typically about half Vcc with some room on either side
Output – sets voltage to Vcc or 0v
Scale determined by processor architecture:
  8-bit: 0-255
  10-bit: 0-1023
  16-bit: 0-65535 – our class project
Value corresponds to the proportional voltage from 0-Vcc
  Input – detects current voltage level
  Output- sets voltage level

## Slide 6: Other Input/Output Types
There are other methods of input/output available:
  I2C/SPI/UART
    Communications with devices
  PWM – Pulse-Width Modulation
    Audio
    LED dimming
    Drive servo motors
And others…
We won’t cover these in class

## Slide 7: Serial Connection
Communication with the board is done via serial connection over USB
  Transferring program code
  Sending/receiving data during runtime
Connection can be made in multiple ways:
  Mac – screen /dev/tty.usbmodem####
  Windows – need to install a terminal program
  Recommended way is to use a code editor that has a built-in serial terminal
    Arduino IDE – for C/C++ coding
    Mu – for Python coding – We will use this one

## Slide 8: Example – Water Filter Controller
Before
RO filter with electric pump
Drain connects to kitchen sink – loud when running
Runs based only on water pressure
Annoying to run during day
After
ESP8266
  Built-in WIFI
Output – digital connection to Relay board
  To switch 120V
Input – Analog connection to Pressure Sensor
Retrieves current time via WIFI
Normally only runs 1-2 am
  Runs during day if pressure is extremely low
Notes: Show water program

## Slide 9: CircuitPython
Python tools & libraries for microcontrollers
  As alternative to using C/C++
Not all microcontroller boards are supported
  However, many are: https://circuitpython.org/downloads
  Our boards already have CircuitPython installed
Aims to make programming these boards easier
  Python is easy to learn
  No compile steps
  Many libraries available
  Just needs a regular text editor and USB connection
No start() or loop() functions – Instead operates just like regular Python code
  Do setup in the beginning
  Enter into a loop for operational code
  When control reaches the end, the program stops

## Slide 10: Example – Traffic Light Simulation
Red/Yellow/Green LEDs, connected to 3 digital outputs
Done two ways:
  ESP8266 – using C
  Trinket M0 (same as our class project uses) – using CircuitPython
10 seconds on green, 3 seconds yellow, 10 seconds red
Notes: Show both versions

## Slide 11: CircuitPython
CircuitPython also supports interactive mode (REPL)
  Connect via USB
  Launch Mu editor
  Open the serial console:
    If the program is running, you will see the output – press Ctrl-C to quit it
  Press Ctrl-D to enter REPL
  Type Python code as usual
  Press Ctrl-D again to quit REPL and go back to the stored program
Notes: Demo REPL – make yellow light blink

## Slide 12: Homework: Install Mu Editor and run example
Download and run the installer
  https://codewith.mu/en/download
Connect the device with USB
  You should see a drive named CIRCUITPY
    Windows users might need to install drivers – if this isn’t showing up or it’s not working correctly, contact me for a coaching call
Run Mu Editor
Download example code
  https://pages.process-solutions-group.com/sites/ds2023/301/3 - arduino and circuitpython/homework.py
Open the file in Mu (or copy/paste into the editor)
Save
  Make sure it saves on the CIRCUITPY drive as code.py
Start the serial console
  You should see numbers being printed
Move the motor mount up and down and the numbers should change
Notes: Go through homework steps