## Slide 1: Advanced Data Science Programming
5. Program the Data Recorder

## Slide 2: Data Recorder Program
The data recorder program will run on your PC to receive the data from the control unit and store it as a CSV file.
Steps:
  Import required modules
  Open serial port
  Set up data storage
  Loop while reading data from serial
    Parse the data and add it to storage
  Handle an interruption from pressing Ctrl-C
  Create a DataFrame
  Write the DataFrame to CSV
  Finally, close serial port
    Can cause conflicts/errors if not closed cleanly before exiting

## Slide 3: Required Modules
os
pandas
serial – needs pyserial package
  To install: pip install pyserial
sys
time

## Slide 4: Using the Serial Port
We’ll use the serial module to interact with the serial port
serial provides a tool to list available ports:
  serial.tools.list_ports.comports()
If only one is available, use it. If more than one, input choice
Open the selected port
  serial.Serial(device, 115200, timeout=1)
Sleep for 2 seconds – some systems need time to complete the connection

## Slide 5: Read the Data
Create a list to store the data
Go into a loop, reading the data line by line
Parse the data into a tuple
Convert to integers and store in the list

## Slide 6: Handle the Interruption
We will continue looping until it is interrupted by pressing Ctrl-C
When that happens, a KeyboardInterrupt error is raised
Use try/except in the loop to catch the error and break out of the loop

## Slide 7: Save as CSV
After the loop is finished, we’ll use Pandas to write the data as CSV via a DataFrame
Create a Dataframe from the list
  Use column names [‘force’,’rpm’]
Use as_csv() to write out the file

## Slide 8: Run on Command Line
Since we’re using ctrl-c to interrupt, this program should be run on command line
  In Anaconda Navigator, go to Environments
  Select the ds2023 environment
  Click the green arrow and select Open Terminal
  Change to the directory containing readserial.py
  Run: python readserial.py
    If more than one serial device is active, select the one with Trinket M0 in the name
  Let the program run while you run the device and adjust the motor mount up and down
  Press ctrl-c
  A file named machinedata.csv should have been written

## Slide 9: Homework
Download the code from the class website and get it running on your device and PC
If you have any issues, contact me for a coaching call